## Slide 1: Adaptive Personal Cooling System
Luka Miljanov (N01624502) & Michael McCorkell (N01500049)
MENG-2530-0NA, Microcontrollers
April 22, 2026

## Slide 2: Project Overview
The Problem
Nearly 500,000 deaths annually from hyperthermia; core temps above 40 °C are a medical emergency
Bedridden, elderly, and ill individuals have diminished thermoregulatory responses (sweating, vasodilation)
Standard fixed-speed fans cannot respond dynamically to changing thermal conditions
What is the APCS?
A prototype embedded system that continuously measures ambient temperature and automatically adjusts fan speed via PID control
Built on the TM4C123GH6PM (ARM Cortex-M4F) microcontroller; interfaces DS18B20 sensor, potentiometer, fan, and I²C LCD
Main Objective
Provide automated, responsive personal cooling that adapts in real time — something a conventional fan cannot do

## Slide 3: Design Requirements & Goals
Performance Targets
Regulate ambient temperature within ±1–2 °C of the user-selected setpoint (20–60 °C range)
Control loop update rate: ~2 seconds; DS18B20 12-bit resolution (0.0625 °C/step)
Fan response from setpoint change to observable airflow: ≤ 3 seconds
Constraints
Platform: TM4C123GH6PM LaunchPad; toolchain: Keil MDK-ARM with CMSIS device pack
Components: off-the-shelf only (DS18B20, 10 kΩ potentiometer, 4-wire 12 V PC fan, I²C LCD)
Firmware in 8 modular C files; no wireless, no battery, no multi-sensor architecture
Success Criteria
PID controller converges to setpoint, fan operates without stall, LCD provides real-time feedback
System gracefully recovers from sensor loss without requiring a hard reset

## Slide 4: Design Process & Architecture
System Block Diagram
Potentiometer → ADC0 Sequencer 3 → Main Loop PID Controller → Soft PWM PB6 → 12 V PC Fan
DS18B20 (1-Wire, PE1) feeds temperature into the PID; I²C LCD (PB2/PB3) shows live status
Firmware Architecture (8 modules)
main.c — control loop; adc.c — potentiometer; ds18b20.c — 1-Wire driver; pwm.c — fan drive
pid.c — discrete PID with anti-windup; lcd.c — I²C display; delay.c — SysTick timing; utils.c — string helpers

## Slide 5: Design Process & Architecture
Hardware Design
SolidWorks rail mount bracket for the PC fan; 3D-printed enclosure with removable lid houses LaunchPad, LCD, and wiring
Potentiometer and LCD accessible through front-panel cutout

## Slide 6: Build Process & Components
Key Components
TM4C123GH6PM LaunchPad — 80 MHz ARM Cortex-M4F, 256 KB flash, 32 KB SRAM
Dallas DS18B20 — ±0.5 °C accuracy, 12-bit resolution, 1-Wire interface on PE1
10 kΩ linear potentiometer — maps 0–3.3 V to 20–60 °C setpoint via ADC0
4-wire 12 V PC fan — dedicated PWM input; hardware PWM on PB6 at 25 kHz
16×2 I²C LCD (addr 0x28) — real-time display of temperature, setpoint, and duty cycle
Assembly Steps
Breadboard wiring: DS18B20 on PE1 with 5 kΩ pull-up; potentiometer wiper to PE3; fan PWM to PB6
SolidWorks CAD → 3D-print enclosure → mount LaunchPad, LCD, and fan rail bracket
Compile with Keil MDK-ARM; flash via on-board ICDI debugger; verify heartbeat LED on PF1

## Slide 7: Challenges & Problem Solving
1. Push-Button vs. PID Design
Course spec required buttons; continuous potentiometer chosen instead — smoother PID setpoint, better for mobility-limited users
2. DS18B20 Power-On Default (85.0 °C)
Sensor pre-loads 0x0550 at startup; firmware detects sentinel, holds PID at zero until real conversion completes
3. 1-Wire Timing Sensitivity
Reset pulse ≥480 µs; write-1 = 6 µs, write-0 = 60 µs; calibrated delayUs() against logic analyzer for reliable presence detection
4. Fan Stall Below 90% Duty
10 Hz PWM on-time too short at low duty; MIN_DUTY clamped at 90%; 500 ms kick-start at 100% overcomes static inertia
5. ADC Noise on Potentiometer
±5–10 LSB jitter even with 64× hardware oversampling; added 8-sample software average to reduce noise below ±1 LSB
6. I²C Initialization Order
LCD corruption when I²C0 init ran before SysTick; fixed by calling SysTick_Init() first in main.c

## Slide 8: Testing & Results
System Performance
PID converged to within ±1–2 °C of setpoint under steady-state lab conditions
Fan response latency: ~2 seconds (750 ms DS18B20 conversion + 20 × 100 ms PWM cycle)
Kick-start eliminated cold-start stall: 100% success vs. ~60% stall rate without it
Fault Tolerance
Sensor disconnect detected within one loop cycle; fan duty set to zero; re-acquisition automatic upon reconnection
Heartbeat LED toggled every loop pass — no watchdog violations or lockups observed in all test sessions
LCD & Display
Real-time display of current temperature, setpoint, and fan duty % confirmed accurate across full 20–60 °C range
Three status codes: normal operation, no-sensor fault, and startup/converting
Limitations
Minor oscillation due to thermal inertia of air mass and coarse 10 Hz PWM update rate

## Slide 9: Live Demonstration
What to Watch For
LCD Line 1: current ambient temperature (from DS18B20) and fan duty % updating in real time
LCD Line 2: setpoint temperature — rotate potentiometer to change target
Fan speed visibly increases as temperature rises above setpoint; slows or stops when below
Demo Steps
1. Power on — observe splash screen, then sensor detection and first reading on LCD
2. Rotate potentiometer to lower setpoint below ambient — fan spins up, duty shown on display
3. Rotate to raise setpoint above ambient — fan slows; observe kick-start on next spin-up
4. Briefly disconnect DS18B20 wire — LCD shows NO SENSOR; reconnect and watch auto-recovery
Backup
Video recording of full demo available if live hardware cannot be presented

## Slide 10: Future Improvements
Hardware Upgrades
Replace software PWM with TM4C123GH6PM hardware PWM module (25 kHz) for finer duty resolution and decoupled loop timing
Replace ambient DS18B20 with a skin-contact NTC thermistor patch for direct body temperature monitoring
Add Bluetooth Low Energy (BLE) module for smartphone setpoint control — critical for bedridden users
Software & Control
Implement adaptive PID gain scheduling: larger Kp at high error, smaller near setpoint to reduce oscillation
Add multi-sensor support for zone-based cooling in larger enclosures
Productization
Formal DS18B20 calibration against NIST-traceable reference (prerequisite for clinical deployment)
Battery-powered operation and form-factor miniaturization for wearable/portable applications

## Slide 11: Conclusion
What Was Built
A fully functional closed-loop personal cooling system on the TM4C123GH6PM using DS18B20, PID, software PWM, and I²C LCD
Firmware organized across 8 modular C source files; compiled with Keil MDK-ARM
Was It Successful?
Yes — PID converged within ±1–2 °C; fan operated without stall; system recovered from sensor faults automatically
Validates PID-based closed-loop control on resource-constrained ARM Cortex-M4 hardware for thermal management
Key Takeaways
Hands-on experience with 1-Wire protocol, I²C initialization, discrete PID tuning, and motor drive behavior
Prototype establishes a foundation for a medically meaningful personal cooling device with further development

## Slide 12: Questions?

## Slide 13: Thank You!!